## Slide 1
Fuzzy Controlled Adaptive Follow the Gap Obstacle Avoidance Algorithm
Bilal Yucel, Abdurrahman Yilmaz, Osman Ervan, Prof. Dr. Hakan Temeltas
19.11.2021

## Slide 2
MOTIVATION
Obstacle avoidance is critical for robots
To develop a method that allows robots operate in any environment
Method shall be operatable with slow processors

## Slide 3
OUTLINE
Simulation Tools
  Robot Operating System(ROS)
  ROS-Gazebo Environment
  ROS-Rviz Monitoring Environment
Fuzzy Controlled Adaptive Follow the Gap Obstacle Avoidance Algorithm
  Follow the Gap(FGM)
  Improved Follow the Gap(I-FGM)
  Adaptive Follow the Gap(A-FGM)
Experimental Results
  Success Rate Increment
  Efficiency Improvement
  Outdoor Performance Test
Conclusion and Future Works

## Slide 4
BASICS of ROS
Nodes
Executable processors
Perform tasks(Capture video, Image processings)
Topic
Output of nodes that is published and can be subscribed
Consist of message
Message
Contains variable values
Has various types such as integer, float and boolean
Ros message types such as geometry_msgs/Twist, sensor_msgs/PointCloud
Architecture

## Slide 5
SIMULATION TOOLS
Modelling environments, robots and sensors
Physics Engine
Gazebo
Rviz
Sensor data monitoring
Control and commands
Package
Pre-build libraries

## Slide 6
SIMULATION ENVIRONMENT
Gazebo and Rviz View
Image Processing
Camera
Deptimage_to_laserscan package
Processing
Avoidance algorithm
Dept Image
2D Laser Scan
Obstacle Position

## Slide 7
FUZZY CONTROLLED A-FGM OBSTACLE AVOIDANCE ALGORITHM
Advantages
Easy to tune
Dynamic response
No local minimum problem
Low computational Load
Follow the Gap Method
Priorities
Gap size
Safety
Disadvantages
Long trajectories
Failure of reaching goal in some cases

## Slide 8
FUZZY CONTROLLED A-FGM OBSTACLE AVOIDANCE ALGORITHM
Improved Follow the Gap Method
Advantages
Shorten trajectories for some cases
Disadvantages
The average safety metric drops
Where is the minimum distance to obstacle and is the angle between midpoint and goal point

## Slide 9
FUZZY CONTROLLED A-FGM OBSTACLE AVOIDANCE ALGORITHM
Failure of Reaching Goal
Longer Turn Radius

## Slide 10
FUZZY CONTROLLED A-FGM OBSTACLE AVOIDANCE ALGORITHM
NE: Near, MI: Middle, F: Far, NA: Narrow, ME: Medium, W: Wide, S: Short, M: Mean, L: Long
Problems
Algorithm fails when there is an obstacle near to the goal point
Early consideration of obstacles causes longer trajectories
Solution
Tuning a consideration radius() based on distance to the goal point() and angle to the nearest obstacle()
Fuzzy Logic Rule Table and Membership Functions

## Slide 11
SIMULATION RESULTS
Failure of Reaching Goal
A-FGM

## Slide 12
SIMULATION RESULTS
Longer Turn Radius

## Slide 13
SIMULATION ENVIRONMENT
Outdoor Environment
Detailed Plot of Movement

## Slide 14
SIMULATION ENVIRONMENT
Detailed Plot of Movement
Alternation of Consideration Radius

## Slide 15
CONCLUSION AND FUTURE WORK
Conclusion
The failure problem of reaching to goal when a near obstacle exists is solved
Efficiency is increased by reducing the turning radius
Outdoor success rate is improved
Future Work
Verification with simulation algorithms
Obstacle tracking can improve overall efficiency

## Slide 16
Thank you for your attention!
Questions, Comments and Discussions
19.11.2021